## Slide 1: RELAXATION OF STANDARDS
County Roads and Municipal Streets
Neb. Rev. Stat. 39-2113
Boards - Liaison Services Section
https://dot.nebraska.gov/business-center/lpa/boards-liaison/nbcs/downloads/
Chapter 2
Tab 8.3
Notes: 9/17/2022 changed animations on slides 3 and 11. Added subtitle to Slide 16.
9/11/2022 updated Slide 1 with 3-ring binder Tab number. Slide 8 minor change.
10/13/2021 added web link to slides 22 and 27
8/15/2021 updated slides 9, 13, and 17
6/23/2021 added web link on slide 3
4/24/2021 added slides 21 thru 27. Slides 21 thru 26 are about Practical Design. Slide 27 is about NBCS Authority to Conduct Business.
2/1/2020 Updated. Slide 8 minor changes. Previous version 8/14/2019.
8/14/2019 Updated. Previous version dated 2/3/2019. Four slides affected. Slides 1, 5 17 and 19 were updated, typically web links.

## Slide 2: Chapter 2 (428 NAC 2) Procedures for Standards How it is Organized
Title 428 Table of Contents
Slide 2
428 NAC 2-004, Pages 92-94
Notes: The next several screens provide information on Nebraska’s Relaxation of Standards requirements and process.
These are covered in Section 004 of Chapter 2, pages 92-94, including 94a and 94b
NOT FOR AUDIO
The Board is responsible for setting standards and granting or denying relaxation of standards requests.

## Slide 3: Minimum Design Standards are
Attributes established as acceptable by NBCS
428 NAC 2-001
Slide 3
NBCS Standards
Notes: 9/17/2022 change animations.
6/23/2021 Added weblink to the MDS on the Secretary of State website.
The NBCS expresses the level, ideal, or basis, as attributes, mostly as key criteria, and sets values for each criteria depending on the general category (urban or rural), functional classification and other factors.
NOT FOR AUDIO
Standard: attributes (dimensions, speed and design loading) established as acceptable by an authority (NBCS). [A means of determining what a thing should be. Etymology: extendere (Latin), metaphoric, the royal standard coming to stand for royal authority in matters like setting weights and measures. Hence the meaning "authoritative or recognized exemplar of quality or correctness" (late 15c.). Synonyms: criterion, gauge, yardstick, touchstone. ]

## Slide 4
Slide 4
Why Have Design Standards?
  Safer design, driver expectations, reliability
  A primary means to achieve a high-quality product
  Determine systemwide needs
  Required by Authority
    23 CFR 625
    Neb.Rev.Stat. §39-2113
    Local Ordinances and Laws
NBCS Standards
Notes: Minimum design standards try to achieve
Safer designs,
Meet driver expectations
And Improve the reliability of the highway, road and street network
Standards are a primary means of achieving a high-quality product,
although there is a lot more to designing a road or street than just meeting minimum standards.
Standards are a way of benchmarking system-wide needs
And standards are required by authority, by
The Federal government
The Nebraska Legislature
And possibly local ordinances and laws as well.
That concludes the brief overview on Minimum Design Standards. For more detailed information, go to the next video in this series.
NOT FOR AUDIO
Jim Knott’s 2009 slide
Meeting standards:
is a primary means by which a resultant high-quality roadway will be produced. [NOT 100% FOOLPROOF AND NOT THE ONLY MEANS! – GOOD DESIGN WORK IS THE ONLY MEANS!] Designers are trained to use accepted controlling criteria throughout the project development process.
decreases the probability that safety or traffic operational problems will develop. Using design values that lie within typical ranges thus provides some quality control and a reduced risk.

## Slide 5: Construction Standards
2017 NDOT Standard Specifications for Construction
  Required for:
    functional classifications higher than Local, or for
    any work or project
      on the National Highway System, or
      uses Federal funds
Non-NDOT specifications acceptable off the National Highway System
  must be “equivalent in quality” and, if so,
  submittal for NBCS approval is not required
Slide 5
Minimum Construction Standards
428 NAC 2-002, Page 87
https://dot.nebraska.gov/media/10343/2017-specbook.pdf
Notes: 8/14/2019 Updated web link to spec book.
The Nebraska Department of Transportation 2007 Standard Specifications for Construction are
Required for highways, roads and streets with functional classifications higher than Local, or for any work or project on the National Highway System, or any project that is funded in part or entirely with Federal funds no matter what the functional classification is.
And are advisory, i.e. non-mandatory, for functional classifications Local, Scenic-Recreation Local, Minimum Maintenance and Remote Residential.
The 2017 Standard Specifications for Construction are online, at the web link shown on the screen. Standards currently (2/20/2018) indicate 2007 Standard Specifications for Construction; that needs to be updated (public hearing process).
You get to that link as follows:
From the NDOT home page, under the Business Center tab, Contractor Information
Select Contractor’s Corner. Then select Reference Manuals.
Then select the link called “2007 Standard Specifications for Construction”
The regulation recognizes that a city or county may have its own standard construction specifications.
It allows those specifications to be used on city streets and county roads, in lieu of NDOT’s 2007 Standard Specifications for Construction if those specifications are “equivalent in quality” to NDOT’s 2007 Standard Specifications for Construction, and the work or project is not on the National Highway System.
Lack of attention to good construction standards can lead to early failure of your facility, i.e. a shortened life cycle.
That concludes this discussion on Minimum Construction Standards, 428 NAC 2-002.

## Slide 6: Minimum Maintenance Standards
Definition of Maintenance, p 88
Limits of Maintenance, p 88
  Nothing Extensive or Costly (428 NAC 2-003.01C5, p 89)
Physical Maintenance activities, pages 88-91
Minimum Maintenance Standards
428 NAC 2-003, Pages 88-91
Notes: Elements included in the Minimum Maintenance Standards are:
A definition of Maintenance, on page 88
Limits of Maintenance, also on page 88, the limits being necessary to emphasize that activities beyond Maintenance require the application of other standards, i.e. the Minimum Design Standards in Section 001.
The paragraph at the bottom of page 89 mentions that operations which are “extensive or costly” should not be charged to maintenance but to construction.
Routine Physical Maintenance activities are listed on pages 88-91, for roadway surfaces, shoulders and side road approaches, roadside and drainage, and structures.

## Slide 7: Relaxation of Standards What is it?
A documented decision that has NBCS approval to design, construct or maintain an element or segment of a highway, street or road that does not meet a requirement, value or range of values established by the NBCS standards.
Relaxation of Standards
Slide 7
Design Exception
Generally, within work termini
§39-2113
428 NAC 2-004, Pages 92-94
Notes: A relaxation of standards is a decision approved by the Board for a requirement, value or range of values in 428 NAC 2, Procedures for Standards. It applies to sections 001, 002, and 003 of Chapter 2 – Design, Construction and Maintenance standards.
“Relaxation of Standards” is the term used in state statutes.
It is the equivalent of a “Design Exception” – terminology used by the Federal government and others.
NOT FOR AUDIO
If something beyond the work termini do not meet standards, generally speaking the Board does not expect a request for a relaxation of standards.

## Slide 8: Why Would a Relaxation of Standards be Necessary?
Applying standards: a special hardship due to peculiar, special or unique local situations
Many reasons, or combinations of reasons
  • Affect on the natural environment
  • Social or right-of-way impacts
  • Preservation of historic or cultural resources
  • Sensitivity to context, or community values
  • Construction costs
Relaxation of Standards
Slide 8
§39-2113
428 NAC 2-004, Pages 92-94
Notes: 9/11/2022 first bullet added colon.
2/1/2020 Updated wording slightly changed “impacts” to “affect” on the natural environment.
To achieve a highway, road or street design that is well[-balanced (safety, operations, environmental impacts and cost), it may not always be possible to meet standards. There is a wide variety of site-specific conditions and constraints that can be encountered.
State law refers to a special hardship because of peculiar, special or unique local situations.
There can be many reasons for requesting a relaxation of standards.
It may be a severe impacts to the environment, or to something of historic or cultural value, or requiring acquisition of a lot of right-of-way. It could also be costs.
NOT FOR AUDIO
From FHWA’s Mitigation Strategies for Design Exceptions, July 2007 publication:
For many situations, there is sufficient flexibility within the design criteria to achieve a balanced design and still meet minimum values.
It must be recognized, however, that to achieve a well-balanced design (safety, operations, environmental impacts and cost), it is not always possible to meet design criteria. There is a wide variety of site-specific conditions and constraints that designers encounter. Roadways have a multitude of contexts. Establishing design criteria that cover every possible situation, each with a unique set of constraints and objectives, is not possible. On occasion, designers encounter situations in which the appropriate solution may suggest that using a design value or dimension outside the normal range of practice is necessary. Arriving at this conclusion requires the designer to understand how design criteria affect safety and operations.

## Slide 9: Relaxation of MDS Required When . . .
A standard value or range or requirement in
MDS Tables (pages 55-86)
MDS Notes (requirements in bold font) – pages 47-54
cannot be met due to a special hardship.
428 NAC 2-001.03B Note 1, Page 47
Note 1 (new)
Slide 9
Notes: 8/15/2021 added page numbers for MDS tables
Regarding design standards, 428 NAC 2-001, a relaxation of standards is required if a requirement, or standard value or range cannot be met because of a special hardship.
This applies to MDS
tables
notes –
In the notes for county roads and municipal streets standards, [in 428 NAC 2-001.03B (subsection 3, part B)], on pages 47-54, the requirements and standard values are in bold font
Anything not in bold font is information and guidance for which it would not be appropriate to request a relaxation of standards

## Slide 10: Who Can Request a Relaxation of Standards?
The NDOT, a county or a municipality
Any other interested party, for a road classified as Scenic-Recreation [ref. §39-2103(4) and §39-2113(2)]
Relaxation of Standards
§39-2113(6)
428 NAC 2-004, Pages 92-94
Slide 10
§39-2113(6)
Notes: A relaxation of standards can be requested by
The NDOT
A County
A Municipality
Or, for a road classified as Scenic-Recreation, by any other interested party if the party believes that the application of Scenic-Recreation standards would defeat the purpose of the Scenic-Recreation classification (39-2103 and 39-2113(2))
NOT FOR AUDIO
39-2113
(6) Any county or municipality which believes that the application of standards for any functional classification to any segment of highway, road, or street would work a special hardship, or any other interested party which believes that the application of standards for scenic-recreation roads and highways to any segment of highway, road, or street would defeat the purpose of the scenic-recreation functional classification contained in section 39-2103, may request the board to relax the standards for such segment.

## Slide 11: What is the Process?
File a request with the Secretary of the Board.
The Secretary of the Board sets a hearing date for no later than 60 days after the filing of a complete request.
A notice is given to the requesting party at least ten (10) days prior to the hearing.
Relaxation of Standards
428 NAC 2-004D, E and F, Page 94
Timely submittal is important to avoid delays!
Notes: 9/17/2022 change animations.
Filing a request with the Secretary of the Board starts the process.
The Secretary of the Board must set a hearing date for the request no later than sixty (60) days after the filing of a request that is complete. The requirements of a complete submittal will be discussed later in this presentation.
A notice confirming the date is provided to the requesting party at least ten (10) days prior to the hearing.
As you look at the possibility of up to 60 days until the hearing, note that it is important to identify the need for a relaxation of standards request as soon as you possibly can, and then promptly submit it to the Secretary of the Board. [428 NAC 2-004.01D on page 94]
That includes planning and designing a work or project. The need for a request should be determined as early in the design process as possible, hopefully in the preliminary engineering phase.

## Slide 12: What is the Process? (continued)
On the date of the hearing, the NBCS
  Considers all information submitted
  Votes (needs an affirmative vote of at least 6 Board members)
    to grant or deny, in whole or in part, or to
    continue the hearing until the next Board meeting
Decision can be appealed in accordance with the Administrative Procedures Act
Relaxation of Standards
428 NAC 2-004D, E and F, Page 94
Notes: At the hearing, the Board can grant or deny the request, in whole or in part, or continue the hearing to the next Board meeting.
The Board’s decision can be appealed.

## Slide 13: NBCS Requirements for Relaxation of Standards Requests
Thorough analysis and documentation is required
  18 basic submittal requirements (01A1 - 01A18)
A relaxation that is granted becomes the minimum standard for that roadway segment or bridge, until circumstances change
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: 8/15/2021 added regulation paragraph numbers for the 18 basic submittal requirements
There are a minimum of 18 requirements in order to have a complete submission for a request for a relaxation of standards. These are listed starting at the bottom of page 92, sub parts 1 through 18 ending on page 94.
There are additional requirements on page 94 for the Scenic-Recreation classification and for Low-water Stream Crossings and Fords in Parts B and C, respectively.
Whatever the Board grants for a design standard, it becomes the minimum standard for that roadway segment or bridge, until circumstances change.
This could be a change of traffic patterns and volumes, a change of functional classification and other reasons.

## Slide 14: Tips for Submitting a Relaxation of Standards Request
Be clear, be specific about what you are requesting (state it in the opening paragraph!) and be complete!
  Table Values and Notes
Use terminology that the Board is familiar with, i.e. terminology from 428 NAC 2
Notes 12-14, Note 16 (b), Note 22 – if meet those requirements, no request is needed!
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: Terminology – recent request used “Reconditioned” roadway – what is that?

## Slide 15: EXAMPLE
Relaxation of Standards
For Hypothetical Project
Based on Petersburg NE Project
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: The penalty for not meeting standards is a 10% reduction in next year’s Highway Allocation fund distributions.
If a work or project is funded in part, or entirely, using Federal funds, and does not meet standards, there is a risk of losing some or all of that Federal funding.
That concludes this discussion on Relaxation of Standards, 428 NAC 2-004

## Slide 16: EXAMPLE – TABLE FORMAT Good Way to Communicate Request to the NBCS
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: 9/17/2022 added subtitle to audience understands the point of this slide.
A good way to communicate with the Board is to specify all locations that do not meet standards and for which a relaxation of standards is being requested.
This example is the Petersburg NE project, the 110th St segment.

## Slide 17: Request SNAFU’s
Not understandable enough for Board members
Plans – not complete, not correct, not readable
Other Documents – incomplete (e.g. design speed for VC), not anticipating obvious questions the Board may have, missing typical sections and signing plans
Conflicts across various documents (including Resolution)
Wrong standards applied
Request doesn’t include all criteria and notes that it should, or includes criteria it doesn’t need to
Not enough detail describing special hardship
Adjacent segments – not addressed
No mitigation?
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: 8/15/2021 added #5 not enough detail describing special hardship and a few other changes based on the latest relaxation request
8/14/2019 Updated, added LB82 note in script.
Not understandable enough for Board members – YOU know they project, THEY (BOARD MEMBERS) probably don’t know anything about it, so you need to make it easy for them to understand by giving even what seems to you to be obvious conclusions.
Making documents easy for Board members to understand – too wordy, should use tables, project begin and project end points not labelled, alternatives on plans not labelled.
Incomplete or unreadable or incorrect plans (Existing typical section missing)
Incorrect plans (Fixed Obstacle Clearance vs. HCZ)The
LPA Resolution incorrect, or conflicts with other information presented
Incorrect Work/Project Form - wrong functional classification, wrong standards, etc. LB82 DID AWAY WITH W/P FORM!!!!
Plans and LPA resolution and LPA Relaxation Request conflict (10 ft. lane width vs. 11 ft. lane width, or 4 ft shoulders vs 2 ft shoulders)
Adjacent sections (beyond construction limits) not addressed (a VC a hundred feet away does not meet MDS)
No information on features planned to mitigate the effects of not meeting the MDS
Incomplete information (design speed for vertical curve not meeting MDS, no mention of hydraulic analysis)
Not asking for a relaxation, but should - design speed, or stopping sight distance for a VC not meeting MDS, or justifying not requesting a relaxation for a design value not meeting MDS based on an industry publication - one request didn't ask for relaxations for five (5) MDS criteria that should have been included)
Asking for a relaxation unnecessarily - Note 14 allows steeper grades for short tangent lengths, or HCZ accepted via paragraph (b)
Not anticipating the questions that the Board will likely ask: MDS standard for stopping sight distance is based on level terrain but street has a steep grade (Board would ask if that was considered, or how it is justified)
Applying the wrong standards (3R instead of N&R)
Not explaining the special hardship adequately – what is so peculiar or unique or special about it?

## Slide 18: Failure to Meet Standards
Penalty
10% reduction in next year’s State Allocations, for not meeting minimum standards, per §39-2121(3)
Possible loss of Federal Funds (if the work or project if funded in whole or in part with Federal funds)
Relaxation of Standards
428 NAC 2-004, Pages 92-94
Notes: The penalty for not meeting standards is a 10% reduction in next year’s Highway Allocation fund distributions.
If a work or project is funded in part, or entirely, using Federal funds, and does not meet standards, there is a risk of losing some or all of that Federal funding.
That concludes this discussion on Relaxation of Standards, 428 NAC 2-004

## Slide 19
Federal-aid projects may also require a Design Exception from FHWA.
Projects of Division Interest (PoDI) per FHWA/NDOT Stewardship Agreement
In Addition to a
Relaxation of Standards
Slide 19
Notes: 8/14/2019 Updated web link.
A city or county must check with the Local Projects Section, for any Federal-aid project, to see if a Design Exception is necessary in addition to a Relaxation of Standards.

## Slide 20: Relaxation Requests
428 NAC 2-004
18 basic requirements
  428 NAC 2-004.01A1 thru 18
Min. Maint. Roads, Low Water Xngs
Complete submittals
  Public Record
  Legal Document
  Liability
Checklist - handout
Relaxation of Standards
Slide 20
Notes: 5 min

## Slide 21: If NBCS Minimum Standards Cannot Be Met
Relaxation of Standards, for a specific work or project. The NBCS decides these at public Board meetings. Regulated by Title 428, Chapter 2-004
Change the Standards. Requires rulemaking, a process involving public comments and public hearing(s).
Two Options Have Been Available
Slide 21
Now there is a third option available
Multi-Project Program or Strategy
Notes: 4/24/2021 new slide – taken from Practical Design video Power Point.
Transcript
Until recently, if NBCS minimum design or maintenance standards could not be met, there were two options available:
Request a relaxation of standards from the NBCS. OR
Change the standards.
The first option applies to a specific project and is usually requested in the preliminary engineering phase of the project.
The second option requires rulemaking, an extensive effort and therefore occurs only once every few years.
A third option is now available: a multi-project program.
It is NOT a new standard but it DOES allow flexibility with current NBCS standards, and it could be an interim solution potentially leading to changing the standards (option #2) via rulemaking.
It is required that NDOT, counties and municipalities work in cooperation with the NBCS to establish a program, prior to its implementation.
Note that the NBCS does not approve designs, rather, it would be agreeing to allow an entity to not meet certain of its standards.

## Slide 22: §39-2113(7) - from LB82 (2019)
Authorizes certain programs to be developed
  Design: practical, flexible and context sensitive
  Asset preservation, preventative maintenance
Individual projects and works conforming to the program will have Board preapproval
Cooperation between the NBCS and NDOT, counties and municipalities
  develop, support, approve and implement
Slide 22
“Practical Design”
Notes: 10/13/2021 added web link
4/24/2021 new slide – taken from Practical Design video Power Point.
Transcript
NBCS standards are based on criteria – mainly geometric criteria such as lane width, shoulder width, horizontal curvature, and vertical curvature.
If a standard cannot be met for a particular project, counties and cities are required to request a relaxation of standards for that project from the NBCS. This will remain the same.
However, LB82 (passed in 2019), and formalized in state statute 39-2113(7), allows more flexibility in meeting those standards.
A program – which implies multiple projects or works – can now be established; projects or works conforming to such a program would have Board preapproval, eliminating the need for the Board to review and grant a relaxation of standards for each of those individual works or projects.
Strictly speaking, bringing a program or strategy to the NBCS for approval is NOT a relaxation of standards even though it involves not meeting Board standards. A relaxation of standards applies to only one project and is governed by the regulation 428 NAC 2-004.
The terminology used in the state statute, and shown on this slide – practical design, flexible design, context sensitive design, asset preservation – reflect a performance-based approach, in recognition that standards are a good starting point but there are many factors, beyond geometrics, that go into decision-making when designing and constructing highways, roads and streets.
The statute allows the NBCS, NDOT, counties and municipalities to cooperate and agree upon programs based on such design practices, typically referred to as PRACTICAL DESIGN.

## Slide 23: Practical Design
Slide 23
Primary problem and need
Extend the life of assets
Substantial Overall Benefit: Cost vs Performance
  Cost/Benefit Analyses
  Best Value Analyses
  Life Cycle Analyses
Notes: 4/24/2021 new slide – taken from Practical Design video Power Point.
Transcript
PRACTICAL DESIGN IS a nationwide movement or trend to rebalance limited funds toward the need, or the problem, where asset preservation and safety performance are the focus.
Strict adherence to geometric, dimensional criteria could lead to overdesign, resulting in unnecessary costs, or may be inappropriate for the roadway context.
Practical design emphasizes the primary problem and need, extending the life of the asset, and on benefits: cost vs performance.
Focusing the funding on the primary problem or need in constructing projects intends to provide substantial overall benefit at a reasonable cost to the public. This allows savings to be invested in other roadways, thus improving the overall roadway network.
Practical design tries to get at WHAT IS THE OVERALL BENEFIT TO THE PUBLIC?
Proving that typically involves cost benefit analyses, best value analyses and/or lifecycle analyses.
It may take into account the needs and values of the community; be it county, municipality or whatever local community to enable projects that balance safety while making the improvements in a manner that fits the surroundings and provides an overall benefit to the public.
[Context sensitive – i.e. the road up into the mountains, the city street accommodating pedestrians, bicyclists and transit. ]

## Slide 24: Why Develop a Program?
“If it ain’t broke, don’t fix it.” No significant, relevant crash history.
Safety performance, driver expectancy and uniformity are not
  substantially or materially improved by building to standards, or
  reduced because added features adequately compensate.
Community needs and values (context sensitive design) are a primary need.
A recurring situation where meeting NBCS standards costs more than it benefits
such as . . .
Slide 24
Notes: 4/24/2021 new slide – taken from Practical Design video Power Point.
Transcript
There are different reasons to request a program. Usually these are recurring situations on roadways similar to each other, having similar characteristics, and that applying an NBCS standard costs more than it benefits. Such as
If it ain’t broke, don’t fix it – there is no significant, relevant crash history, and building to the standard just for the sake of satisfying the standard would be overbuilding.
Safety performance, driver expectancy and uniformity are not substantially or materially improved by building to the standard. Mitigation features introduced with the design might offset the change in performance resulting from not meeting the standard. For example, adding rumble strips at the edge line.
If community needs and values are primary considerations, such as context sensitive design. The benefits of context sensitive design are often more qualitative than quantitative.

## Slide 25: Programs and Safety
Safety performance is the uppermost concern of the NBCS.
  Programs don’t change that!
Safety conscious design is key – embed safety as part of design process.
Programs focus $ on safety issues alongside problems and needs
Slide 25
Notes: 4/24/2021 new slide – taken from Practical Design video Power Point.
Transcript
As you may have realized from the previous slide,
Practical Design is not a work around, or a way of avoiding standards.
IT DOESN’T SACRIFICE SAFETY!
A program is NOT a clever way of avoiding standards.
Safety is perhaps the uppermost concern of the NBCS and programs won’t change that.
So continue embedding safety conscious design as part of your design process
And giving due consideration to safety issues

## Slide 26: Primary Considerations
Achieves a substantial overall benefit or a “net” positive benefit.
Roadway is already reasonably improved.
Focuses funding on the primary problem or need.
Reasonably consistent with driver expectancy and system uniformity.
Results in cost savings that could be applied toward other capital and/or system preservations improvements.
Slide 26
Notes: 4/24/2021 new slide – taken from Practical Design video Power Point. Notes taken from five slides from the Practical Design video Power Point.
Transcript
When considering a request for a program, the Board anticipates focusing on five primary considerations.
The following is a brief discussion of each.
A substantial overall benefit or a “net” overall benefit is required by the statute 39-2113(7). In not meeting standards, the applicant must quantify the benefits of the strategy or, in the case of context sensitive design, qualitatively state the benefits. The Board will want some assurance that safety performance, driver expectancy and uniformity with other similar roadways in the network are as good or better than the existing design. Analyses must be well thought out and based on industry recognized research and policy, such as AASHTO, TRB, FHWA and other recognized sources, policies and methods.
1969 legislation anticipated, or at least had the stated goal, of upgrading all highways, roads and streets to NBCS standards. For the past fifty years and longer, entities have been working toward this, resulting in today’s system that is in a large part uniform across the state and mostly meeting driver expectancy.
However, some roads may not have been upgraded, often due to lack of funding.
The Board does not anticipate approving a program that accepts such roadways as they are, believing that entities must continue to strive to improve them in terms of safety performance, driver expectancy and uniformity.
There must be reasonable uniformity and satisfaction of driver expectancy existing for roadways included in the request.
One way that may satisfy this consideration is to show that roadways included in the proposed program have been constructed in compliance with historic design standards, whether New, Reconstructed or 3R standards, OR criterium, formal guidelines or the industry’s prevailing standard of care at the time it was constructed or improved.
It is important for applicants to accurately describe the primary problem(s) or need(s) for roadways included in a proposed program, how funding will address those, the net overall benefits, and why it makes good sense to not build to Board design or maintenance standards.
Any proposed program must demonstrate that driver expectancy and system uniformity will be maintained. In other words, drivers won’t be confronted with something unfamiliar or uncharacteristic and roadways will be reasonably like other roadways similarly classified AFTER THE PROJECT(S) ARE BUILT.
One of the cornerstones of practical design is that it allows limited funding to be spread over more improvement or maintenance projects. A proposal therefore should show how the program will improve the overall system or network of roadways. Cost savings alone will not lead to Board approval.
Furthermore, since the program proposes to not meet Board standards, justification must be provided for each non-standard value, based on analysis, industry guidelines, research and/or standards of care; there should be a technical basis for not meeting standards. For example, conformity to guidelines adopted by the American Association of State Highway and Transportation Officials (AASHTO); for NDOT projects and programs, refer to State statute 39-1316.
This screen summarizes primary considerations when the Board decides on proposed programs.
As with the process discussed earlier, the Board may need to adjust over time as experience is gained, but these considerations are a starting point.
A proposal needs to make common sense, and also fit within the context of the entire system or network of roadways.

## Slide 27: Working with the NBCS Communications, Questions, Requests by Phone , Email or Mail
Routine – Board Secretary answers on behalf of Board
Non-routine – MUST be in writing or electronic.
Board Secretary may involve Professional Support, Board Chair and Counsel as needed to resolve.
Reported to Board at subsequent meeting(s).
Not satisfied with response? Take issue to the full Board for resolution.
Slide 27
https://dot.nebraska.gov/media/114875/nbcs-authority-conduct-business.pdf
ndot.blshelp@nebraska.gov
402-479-4436
NDOT Boards-Liaison Services PO Box 94759 Lincoln, NE 68509
Notes: 10/13/2021 added web link for Boards-Liaison Services
4/24/2021 added slide – taken from 304 NBCS topic – Authority to Conduct Business (adopted by Board at its 9/24/2020 meeting)
Non-routine examples: relaxation of standards requests and inquiries about design standards.
STATE OF NEBRASKA
Board of Public Roads Classifications and Standards (NBCS)
September 24, 2020
Authority to Conduct Business for the Board as it Relates to Communications, Questions and Information Requests of the Board and Staff.
Intent: To establish, for the sake of managing communications and for transparency, a more formal process to receive and respond to questions and inquires of the NBCS.
Routine communications, questions and requests can be discussed and resolved quickly electronically or telephonically by the Secretary of the Board (Secretary) and need not involve the Board. Non-routine communications, questions and requests for information (examples are relaxation of standards requests and inquiries about design standards) should be sent in writing (hard-copy) or electronically (e-mail to ndot.blshelp@nebraska.gov or file-sharing) to the Secretary of the Board for review and determination of proper handling, filing, responding and or answering etc.
Non-routine communications, questions etc, that require a response are to be handled as follows:
The Secretary of the Board (Secretary) shall answer all communications and questions that are within his/her experience and knowledge to resolve. All responses to non-routine communications shall be in writing (hard-copy) or electronic (e-mail or file-sharing), to the requesting individual or entity.
The Nebraska Department of Transportation (NDOT) shall provide supplemental/additional professional engineering (Professional Support) support to the Secretary, and the Secretary shall be authorized to confer with, and request reviews/evaluations, and recommendations from Professional Support on issues that are not routine and are less common, that require additional effort to research and answer. The Secretary, if in agreement, will respond and communicate directly to the individual or entity in writing, as above in 2.a.
For those issues, questions and requests where the Secretary and Professional Support do not agree, or are not sure of an appropriate response, both shall confer with the Chair of the Board and/or Counsel for a proper response, and either the Chair or Secretary shall respond back to the individual or entity, as above in 2.a and b.
Any issues, questions and requests not resolved to the satisfaction of the individual or entity in any of the above steps, may be taken to the full Board for resolution.
All non-routine communications, questions and requests for information will be reported to the Board at any subsequent meetings, for the purpose of transparency in the conduction of the business of the Board. These may not have all details; they may be summaries, relevant portions of communications, and /or listings.

## Slide 28: RELAXATION OF STANDARDS
County Roads and Municipal Streets
Neb. Rev. Stat. 39-2113
Boards - Liaison Services Section
Chapter 2
https://dot.nebraska.gov/business-center/lpa/boards-liaison/nbcs/downloads/